## Slide 1: Side Channel Analysis
June 29, 2022
Ben Janis

## Slide 2: Solving problems for a safer world
© 2020 MITRE #20-2238 8-31-2020
Notes: Thank you for joining us today! We are excited to share with you WHO MITRE is and WHAT we do. We’re going to start off together here in the main room to learn the basics of MITRE and then we’ll head into some breakout rooms to hear about some of the cool work being done at MITRE directly from our engineers!
Without further ado, let’s dive in!
At MITRE, we’re a company of more than 8,000 innovators, deep thinkers, conveners, and problem solvers who come to work every day to tackle the complex threats facing our nation and the world.
With crises and world events unfolding in ways that nobody expects, we pivot quickly, and proactively lead in the public interest.
We know we must pioneer for a better future.

## Slide 3: Mission: mitre's mission-driven teams are dedicated to solving problems FOR A SAFER WORLD
Notes: Through our public-private partnerships and federally funded R&D centers, MITRE works across government and in partnership with industry to tackle challenges to the safety, stability, and well-being of our nation.
We solve tough problems that industry can’t or won’t work on because there isn’t a profit motive or realistic way to get consensus on a solution. We don’t operate with commercial interest. We work in the public interest.
Like developing and supporting the freely available MITRE ATT&CK framework that helps slow down cyber adversaries by exposing the tactics and techniques they use to infiltrate networks.

## Slide 4: Our Impact: Aerospace & Transportation: Airline Traffic Collision Avoidance, Cybersecurity: Threat-informed Defense, Health & Human Services: Data Standards & Interoperability, Homeland Security: Protecting our borders, National Security: GPS/PNT; reliability, accuracy, resiliency, Technology & Innovation: Prototypes & Demonstration
4
Notes: In today's complex world, there will always be a need for more evolution, more creativity, more innovation.
We strengthen the systems that protect our way of life in so many important areas.
Our world is complex. Maybe you didn’t know that MITRE’s innovations power todays GPS systems. Or that we pioneered air traffic collision avoidance systems. Or that we are working to unlock the power of electronic health records to improve patient treatment outcomes.

## Slide 5: MITRE touches your life Every day
Notes: For all of us, the world is a safer place because MITRE exists.

## Slide 6: What is a Side-Channel?

## Slide 7: Side-Channel Example: Store Backroom
How is the backroom organized?
Where are different items located?
What shelves are items stored on?
How many items per bulk box?
Employees Only
By only asking employees for items in the
back and without going in yourself, figure out:

## Slide 8: Side-Channel Analogy
Combo
Acoustic Side-Channel
Power Side-Channel
Crypto Keys
Side-channel analysis (SCA) leverage unavoidable side-effects of performing computation

## Slide 9: Side-Channel Attacks
SCA commonly used to:
  Reverse engineer system operation
  Extract information (e.g., keys)
  Monitor and validate system behavior
Instantaneous Power
Execution Time
Thermal
Acoustic Vibrations
EM Radiation
http://www.itp.net/573498-intel-core-i7-920
https://www.kisspng.com/png-light-electromagnetic-spectrum-electromagnetic-rad-1233022/
https://commons.wikimedia.org/wiki/File:1989_Loma_Prieta_earthquake_seismogram.jpg
https://pixabay.com/en/thermometer-temperature-rainbow-305319/
https://commons.wikimedia.org/wiki/File:Dtjohnnymonkey-Stopwatch-no-shading.svg

## Slide 10: Side-Channel Capture
Side-channel leakage is captured during normal device operation
  Target device is instrumented with sensors (e.g., current monitor)
  Device commanded to perform its sensitive operation
  Captured side-channel data is stored along with the corresponding inputs and outputs
Photo: Tektronix Inc.
Data
Power Consumption
Time
Data-dependent power consumption
Chip Image Source: https://pixabay.com/en/microchip-component-computer-chip-309407/
Battery Image Source: Tango Desktop Project
© 2018 MITRE Corporation

## Slide 11: Side-Channel Workshop: PIN Lock
Scenario:
  A door is secured by a smart door lock
  We want to figure out the 4-digit PIN to open it
  Data available to us:
  Success / failure of PIN guess
  Power consumption of the lock device
  Knowledge that the lock uses strcmp

## Slide 12: Side-Channel Workshop: strcmp
strcmp(correct_pin, incorrect_pin)
Correct PIN:
Pin Guess:
1 2 3 4
1 1 1 1
>

## Slide 13: Side-Channel Workshop: strcmp
strcmp(correct_pin, incorrect_pin)
Correct PIN:
Pin Guess:
1 2 3 4
1 3 1 1
How could we exploit this?
<

## Slide 14: Side-Channel Workshop
https://mybinder.org/v2/gh/janisbent/sc-lab/main?filepath=lab.ipynb

## Slide 15
Ben Janis
btjanis@mitre.org
linkedin.com/in/benjanis